## Slide 1
e/π identification and position resolution of high granularity single sided TRD prototype
M. Târzilă, V. Aprodu, D. Bartoş, A. Bercuci, V. Cătănescu, F. Constantin, G. Caragheorgheopol, M. Petriş, M. Petrovici, L. Prodan, A. Radu, L.Rădulescu, V. Simion, P. Zaharia
2nd European Nuclear Physics Conference, 17-21 September 2012 Bucharest, Romania
  Compressed Baryonic Matter (CBM) experiment – Transition Radiation Detector (TRD) requirements and prototype design
  Pulse height distribution for electrons and pions @ different momenta
  e/π discrimination performance
  Position reconstruction. Systematic study
  Conclusions & Outlook
Hadron Physics Department
NIPNE-Bucharest
(NIHAM)

## Slide 2
CBM - TRD requirements
2
  TRD
  Transition
  Radiation
  Detector
  RICH
  Ring
  Imaging
  Cherenkov
  Detector
  TOF
  Time
  of
  Flight
  ECAL
  Electromagnetic
  Calorimeter
  MVD+STS
Tracking of all charged particles: position resolution ~ 200-300 μm @ high rates (105 part/cm·sec) and high multiplicities
Identification of high energy electrons (γ>2000) with a pion rejection factor > 100 @ 90% electron efficiency
Geometry: 3 stations (3 layers each) positioned @ 4.5, 7.45 and 9 m from target
Current TRD design:
  584 m2 total area
  708 chambers
  737408 readout channels
Mădălina Târzilă, 2nd EuNPC, 20th September 2012
Current TRD structure

## Slide 3
CBM-TRD prototype design
3
readout electrode: PCB 300 μm
triangular shape of pads
readout cell area (0.7 x 2.7)/2 ≈ 1 cm2 , 192 triangular pads and total area of 8 x 69 cm2
Mădălina Târzilă, 2nd EuNPC, 20th September 2012
-single MWPC ( 2 x 4 mm amplification region) + 4 mm drift region
-4 mm anode – cathode gap
-3 mm anode wire pitch (20 µm gold plated W wires)
-1.5 mm cathode wire pitch (70 µm Cu-Be wires)
Sequence of detector assembling

## Slide 4
e
π
4 GeV/c
6 GeV/c
8 GeV/c
e/π discrimination
4
Pulse height distribution for electrons and pions:
π
e
TRD1
TRD2
beam
Mădălina Târzilă, 2nd EuNPC, 20th September 2012
regular foil radiator Reg2 (220 foils 20 μm thick, two consecutive foils are separated by a 250 μm gap) in front of TRD1
Xe-CO2(80% - 20%) gas mixture; HVa = 2000 V; HVd = 800 V
FEE : Fast Analog Signal Processor FASP-VO.1
(A. Caragheorgheopol, D. Bartos, V. Catanescu CBM Meeting, October 2009 , Split)
Test-Beam set-up @ T9 PS CERN 2011

## Slide 5
e/π discrimination – pion rejection factor
5
TRD operationg conditions:
Xe-CO2
HVa = 2000 V
HVd = 800 V
Reg 2 : 220 foils 20 μm thick (two consecutive foils are separated by a 250 μm gap)
pion suppression ≈1% with 7 TRD layers
Mădălina Târzilă, 2nd EuNPC, 20th September 2012
@ p = 4 GeV/c
more information on the backup slide

## Slide 6
d [p.u.]
PRF for TRD1
Position reconstruction – algorithm
6
(track position relative to the center of the pad with maximum charge)
Mădălina Târzilă, 2nd EuNPC, 20th September 2012
Simplified simulations:
effects:
  1.uniform distribution for hit position
  2.Gaussian shape for the charge distribution
  3.pedestal fluctuation
  4.crosstalk between pads
Algorithm:
1.pairing of triangular pads resulting:
a rectangular pad configuration
a tilted pad configuration
2.position across the pads is reconstructed considering clusters of 3 or 2 adjacent pads
3.position along the pads is the intersection of two lines each one parallel with the y coordinate in the systems associated with the pad configurations from above

## Slide 7: Systematic study – simulation I
7
Mădălina Târzilă, 2nd EuNPC, 20th September 2012
-because the Gaussian signal is digitized on a finite interval (given by 3 pads)
systematic errors in position reconstruction
calculate corrections of digitization
beam profile with applied corrections
data
simulation
-data
-simulated
uniformly generated hit position across one pad width
reconstructed position information
cluster shape distributions:

## Slide 8
8
data
simulation
-data
-simulated
Mădălina Târzilă, 2nd EuNPC, 20th September 2012
Systematic study – simulation II
by adding fluctuations and crosstalk
a distribution correction
realistic beam profile
Preliminary results!
-reconstructed measurements
-reconstructed position with correction
-Gaussian fit
missing tail due to a limited number of electronically equipped readout pads
spikes
cluster shape distributions:

## Slide 9: Conclusions & Outlook
Mădălina Târzilă, 2nd EuNPC, 19th September 2012
- the results show:
  e/π discrimination of 1% for 7 TRD layers
  In progress:
  - further systematic studies including the reconstruction along the pads (the y coordinate)
- preparations towards a “real size prototype”
9
  in beam conditions, a position resolution across the pads of ≈ 550 was obtained; this result is compatible with the CBM-TRD requirements
  - not all detector effects were taken into account in simulations
  - lack of information from a “witness” (a detector with a better position resolution)
despite the fact

## Slide 10: Back-up slide
Mădălina Târzilă, 2nd EuNPC, 19th September 2012
10

## Slide 11
Mădălina Târzilă, 2nd EuNPC, 19th September 2012
11
a Rohacell plate between the regular foil radiator and an inner fiber radiator was removed
2011 TRD (2x4+4 mm) prototype
Rohacell plate – support for drift electrode
Pad plane
electrode
e/π discrimination – pion rejection factor